## Slide 1: Control Flow

## Slide 2: Language Mechanisms
Sequencing: intuition of linear order between back-to-back statements
Selection: to represent conditions and choices; if/case/switches
Iteration: repeat some piece of code
Procedural abstraction: logical aggregation of work (and probably data)
Recursion: expression or entity defined in (simpler) terms of itself, directly or indirectly; computational model requires a stack on which to save information

## Slide 3: Language Mechanisms
Concurrency: parts of a program to be executed at the same time, either partially or in full
Exception handing and speculation: program fragment executed with the knowledge and possibility that something could go wrong; mechanisms to handle the wrong part; state back-tracking; different forms of speculation

## Slide 4: Symbol Table
We will implement it as as array of symbols
Each symbol will have:
  Identifier name
  Identifier type
  Identifier width
  Value
Will assume that we have a function: maketemp (table);
Our simple compiler will only support int

## Slide 5: Instruction Table
A list / table / array of instructions
Each instruction will have some number of fields (for us):
  operator
  operand 1
  operand 2
  operand 3
If using 3 operands, it’s called 3-address form (standard terminology)
Will assume we have a function: gencode ( op, a1, a2, a3)

## Slide 6: Program Execution in our Interpreter
We distinguish between instructions being generated at compile time and instructions that will be executed (at run-time)
At compile-time, we need to know how many instructions we have created and/or what is the entry or position of the last instruction generated
At run-time, execution flows mostly linearly:
  Execution position defined by the Program Counter (PC)
  Start with ”first” instruction: PC  0
  Statement Sequencing is achieved by executing instructions in the table code, one after another, and incrementing the Program Counter (PC): PC  PC + 1
  Control-flow constructs (for, while, repeat, do-while, if-then, if-then-else, switch, try, etc): all manipulate the PC by changing it in non-linear fashion

## Slide 7: Instruction Semantics
Operator | a1 | a2 | a3 | Description
OP_ADD | reg0 | reg1 | reg2 | reg0  reg1 + reg2
OP_MUL | reg0 | reg1 | reg2 | reg0  reg1 + reg2
OP_UMIN | reg0 | N/A | reg2 | reg0  - reg2
OP_LT | reg0 | reg1 | reg2 | reg0  reg1 < reg2
OP_JMP | N/A | N/A | instr | pc  instr
OP_JNZ | cond | N/A | instr | If (cond = True) pc  instr
OP_JZ | cond | N/A | instr | If (cond = False) pc  instr
OP_PUSHA | arg |  |  | 
OP_CALL | new_instr | Ret | Old_instr | sp  sp + something; pc  new_instr
OP_LOAD | reg |  | addr | reg  M[addr]
OP_STORE | addr |  | reg | M[addr]  reg

## Slide 8: Sequencing
Essentially, list of statements:
  S1; S2; S3; …; Sn
Effect: S1 executes first, followed by S2, S3, and so on
Compilers will exploit lack of dependencies (information flow) between pairs of statements (e.g. Si and Sj) to reorder them in a legal fashion  similar to out-of-order (OoO) execution
Imperative languages would provide dedicated delimiters: {/}, begin/end
List of statements surrounded by delimiters = block or compounded statement

## Slide 9: Short-Circuit Evaluation
Consider:
if (a < b && b < c) { …}
for (i = 0; i < N && A[i] != NULL; i++)
for (i = 0; A[i] != NULL && i < N; i++)
Idea: avoid unnecessary work
Problem: some of the leftover work could desired side effects
Example: while ( a = my_function(x,a) && x++) { … }
Language dependent
Some languages (I didn’t know this) might have dedicated operators for short-circuit
Ada provides:
and vs and followed by then
or vs or followed by else
Examples:
if (d = 0.0 or else n/d < threshold) then ..
if (p /= null and then p.parent = someval) …
Semantically equivalent to nested ifs, additional logic and control flow

## Slide 10: Control-Flow Productions
assign  id “:=“ expr ;
block  BEGIN stmt_list END ;
stmt  assign
| if
| repeat
| write
| read
;
stmt_list  stmt_list ‘;’ stmt
| stmt
;
body  stmt
| block
;
if  IF ‘(‘ expr ‘)’
THEN body
elsebranch ;
elsebranch  ELSE body
| e
;
repeat  REPEAT body
UNTIL expr ;

## Slide 11: Structured and Unstructured Flow
In memory, all instructions are stored in contiguous fashion
Structured refers refers to using control-flow structures (if-then, for, while, do, repeat, case/switch, exceptions, break/exit)  top-down design
Many control-flow constructs were introduced from Algol 60
Unstructured relies on labels and unconditional jumps (as in assembly)
Label: Identifier serving as placeholder for some instruction position
Jump: some instruction in the PL that forces continuing execution at the target of the jump
Some languages no dot support unstructured control-flow
Unstructured flow considered bad (makes code hard to read, maintain, etc)
Instruction 1
…
Instruction i-1
Instruction i
Instruction i + 1
…
Instruction N

## Slide 12: Repeat Codegen
repeat  REPEAT { $$ = next_instr; }
body
UNTIL
expr {
$$ = gencode (JZ, expr, N/A, $2);
}
Target of
jump instruction
is “backward”, so need to
store temporarily the
instruction
destination that will
be generated “later”

## Slide 13: While Codegen
while  WHILE
{ $$ = next_instr; }
cond
{ $$ = gencode(JZ, $3, N/A, TBDA); }
body
{
gencode(JMP, N/A, N/A, $2);
itable[$4].a3 = next_instr;
}
;
If last_instr
is used instead,
you will get
an infinite loop
Target of jump instruction is “forward”, so need to store temporarily the instruction entry that will be completed later.
Unconditional jump to re-evaluate condition

## Slide 14: IF Codegen
if  IF ‘(‘ expr ‘)’ THEN
{ $$ = gencode(JZ, expr, N/A, TBDA); }
body
{ $$ = gencode (JMP, N/A, N/A, TBDA);
itable[$6].a3 = next_instr;
}
elsebranch
{ itable[$8].a3 = next_instr; }
;
elsebranch  ELSE body
| e
;
Skip the
false-branch
if cond is True
Skip the
true-branch
if cond is false
Targets of both
jump instructions
are “forward”, so need to
store temporarily the
instruction entry that will
be completed later

## Slide 15: Structured and Unstructured Flow
In Basic, the target of the GOTO could also be a line number
break: stops execution of single loop construct in C/C++
continue: skips the remaining instructions in a loop and proceeds with evaluating the condition of the next iteration
Multi-level returns (MLR): some construct that allows to exit from several function calls
Unwinding:
  repair stack, remove corrupted/failed functions, deallocate stack frames
  A lot of book-keeping: state in registers, fetching access links
Think how to implement the break and continue constructs in our compiler
function f1 () {
…
call f2 ();
…
label HERE;
…
}
function f2 ()
{ … call f3 (); …}
function f3 () {
…
if (error) goto HERE;
…
}

## Slide 16: Structured and Unstructured Flow
Exception handling:
  dangerous code + repair code
  Internally, not very different from a switch or for
  Several implicit jumps, depending on what happens, where, and when  control transfer
Similarities between MLR and structured exceptions:
  Control transfer from inner to outer context
  Unwinding stack (functions that failed)
Distinction between (MLR) and structured exceptions:
  Completion of task: success for MLR, failure for exceptions
try {
// dangerous code
} catch (ExceptionType e1) {
// do something
} catch (ExceptionType e2) {
// some other error
}
[ finaly {
// optional
// code to always executed
}
]

## Slide 17: Expression Evaluation
An expression is either a simple object (literal or variable) or some function of these
For the latter, we use the terms operators and operands
Languages provide ”simple”, pre-built math functions via operators
Operators are applied to operands
FYI: ”simple” is relative; compare C vs. Python
Some languages could have more than a single name for an operator, and rely on syntactic sugar to simplify writing; examples:
  Ada: a + b is short for “+”(a,b)
  C++: a+b is short for a.operator+(b) or operator+(a,b)
  Other (some language): 0 <= i,j < N could be short for 0 <= i < N and 0 <= j < N

## Slide 18: Expression Evaluation
Language defines the operator notation: infix, prefix, postfix
  prefix: op a b, or op(a,b) or (op a b)
  infix: a op b
  postfix: a b op
Most imperative languages use infix notation for binary operators and prefix notation for unary ones
Lisp uses prefix notation for all functions, in Cambridge Polish notation:
  (* (+ 1 3) 2) == (1 + 3)*2
  (append a b c my_list)
ML-family languages avoid parentheses, except for disambiguation:
  max (2 + 3) 4;

## Slide 19: Precedence and Associativity
In what order should operators be evaluated?
Example with Fortran: a + b * c ** d ** e / f
Choices:
  ((((a + b) * c ) ** d) ** e) / f or
  a + (((b * c) **) ** (e/f))
  a + ((b * (c ** (d ** e))) / f)
Fortran opts for the last one, exponentiation being right associative, and having higher precedence than multiplicative operators
Recall:
  Precedence: in which order should operators of different categories be evaluated, e.g. {+,-} and {*,/}
  Associativity: in what order should operations in the same category be evaluated, i.e. left-to-right or right-to-left?

## Slide 20: Precedence and Associativity
I like this statement from the book:
  ”The precedence structure of C (…, of its descendants, C++, Java, C#) is substantially richer than that of most other languages …”
And this other statement:
  “It is probably fair to say that most C programmers do not remember all of their language’s precedence levels.”
When in doubt: consult the language reference or add parentheses
Now, compare with Pascal:
  if (A < B and C < D) then (* good luck *)

## Slide 21: Precedence and Associativity
Rules for basic arithmetic operators are mostly standard and uniform across languages, i.e. associate left-to-right
Example 1: 9 – 3 – 2 == 4, not 8
Example 2 (Fortran): 4 ** 3 ** 2 == 4 ** 9 and not 256 ** 2
Example 3 (Ada): exponentiation does not associate, so explicit parenthesis are necessary: (4 ** 3) ** 2 or 4 ** (3 ** 2)
Example 4 (C): multiple assignments as ”a = b = a + c”, obviously is right associative

## Slide 22
Taken from the book
“Programming
Language Pragmatics”
by Michael L. Scoot

## Slide 23: Assignments
Pure functional languages:
  rely solely on expressions
  computation = expression evaluation
  complex computations employ recursion to generate values, expressions and contexts
Imperative programming:
  Attempts to model memory state
  Sequences of changes/updates on/to memory
  Assignment = abstraction for memory write
  Assignments = {value, references/address}  value stored to address

## Slide 24: Assignments
Side effect: influence of a program construct on subsequent computations
Best example, the assignment in imperative languages, two parts:
  right-hand side evaluation
  more importantly, writing the result of the rhs expression to the address of the variable on the lhs
Some PL distinguish between expressions and statements:
  expressions may have side effects, e.g. a = ++c * 2
  statements used to provide side effects
Purely functional languages: no side effects, value of expression depends only on the referencing environment

## Slide 25: References and Values
Consider the following assignments in C:
  d = a;
  a = b + c;
RHS: value
LHS: location / address, where to store something
Variables are named containers for values
Distinction between l-values (address) and r-values (proper values, which could be addresses)
Bunch of subtle rules:
  not all expressions can be l-values  why?
  Compare two (potential) assignments: 2 + 3 = a and a = 2 + 3, when will these be valid (if ever)
  Not all l-values are simple names, consider:
    (f(a)+3)->b[c] = 2;

## Slide 26: References and Values
Value model vs reference model
Value model: values flow from rhs to lhs
Reference model:
  All variables are l-values
  Variables automatically dereferenced when they appear in r-value contexts (equivalent to doing *variable in C)
  Becomes important to distinguish 2 cases:
    variables that refer to the same object
    variables that refer to different objects, but with the same value
b := 2;
c := b;
a := b + c;
Java == and equals
Pascal and Clu example
C example: int a; int * ptra;

## Slide 27: References and Values
Reference Model
a := b + c; // Apparently as in Clu
a, b and c are essentially addresses
Actions for the above:
Get the value stored in the address of b
Get the value stored in the address of c
Compute new value
Store the value in the address of a
Value Model
Consider: a = b + c; // in C
Variables in rhs have values associated to them,
so fetching their value is automatic
Actions for the above:
Get the address associated to b
Dereference the address of b and get the value stored there
Repeat the above for c
Compute new value
Store value at the address of a (lhs)
Read page 232, example 6.16: Boxing

## Slide 28: Assignment Operators
Assignment operators modify memory:
  +=
  *=
  op=
Advantage:
  address calculation performed just once
  simplifies code (we write a lot of something = something + somethingelse)
C provides an assignment operator for each of its binary arithmetic and bit-wise operators, for a total of 10
  also prefix and postfix [in|de]crements: var++, ++var, var-- and –var
Prefix form: syntactic sugar for += and -=

## Slide 29: Assignment Operators
Postfix form: NOT syntactic sugar, i.e. has different semantics. Consider:
  *p++ = *q++;
The above copies values from q to p, then advances both pointers

## Slide 30: Initialization
Not all (imperative) languages provide mechanisms for declaration + initialization (a la c  int c = (2 * something);)
Useful to initialize variables:
  static variables local to subroutines need an initial value (usually 0)
  Initialized static variables can use global memory
  Avoid computational errors
Most languages will have mechanisms to initialize variables for pre-built datatypes
Special mechanisms for “aggregate” types, i.e. arrays, structures
Initialization saves time only for statically allocated variables, not for stack variables nor for heap variables

## Slide 31: Definite Assignment
Uses the (static) control flow of the program
Conservative analysis
Considers every possible execution path in the program
Languages like java use this
Example:
int i;
int j = 3;
…
if (j > 0) {
i = 2;
}
…
if (j < 0) {
// do something with i
}
?

## Slide 32: Ordering in Expressions
Precedence and associativity define order in which binary infix operators are evaluated
  Do not necessarily specify orders in which operands are evaluated
Example 1: a – g(b) – c * d
Equivalent to : ( a – g(b)) - (c * d)
But: which one is evaluated first: (a – g(b)) or (c * d)
Example 2: f(a, g(b), h(c))
In which order are the arguments evaluated?
This is important because of:
  side effects
  Code speed
Usually this is “implementation dependent”
Java and C# evaluate arguments from left to right